## Slide 1: Auto Test System Introduction

## Slide 2: Scope
To shorten test cycle time and quickly get data log.

## Slide 3: Need to know before auto test
Only new file creation can trigger tool. Re-transfer file will not trigger.

## Slide 4: Mechanism
As Is
To Be
Test Plan
Test Program
Data log
Step1
Fuji provide test plan
Step2
Orange uses tool to generate test program
Step3
Orange sets test environment and run test program to get data log
Step1
Orange sets test environment
Step2
Fuji provide test plan
Step3
Tool automatically generate test program and get data log
Test Plan
Test Program
Data log

## Slide 5: How to set Auto Test System
Step1 : To close all excel and igxl application in the tester. If not, tool will show error message.
Step2 : To define watching folder, that can contains sub folder for different projects.
(Default folder : U:\TP-to-C651\PatternValidation\Input)
Step3 : To click “Set” button to open test environment window.
Step4 : To defining all input files, then click “Save” button to create Setting.ini. (One project can contain serval sub folders, but only the folder contains Setting.ini can trigger auto test)
Step5 : To click “Watching” button, then wait user deliver new input test. Auto test system will be a tray icon on the right side of the taskbar
test environment window
tray icon
step2
step3
step5
Can set for diff. test case.(ex. CP1/CP2)
step1
step4

## Slide 6: Format
Header
  Use/Not Use
    Not Use will be ignored.
  Comment
    Just record by user and Tool will do nothing.
  Test instance name
    To generate patset and instance name. If it is deplumation name, and tool will rename by
    [Sheet]_[Row#]_Test instance name
  AI type
    Support for Data log/1D/2D
  Data logging setting
    512 FC
    NA
    DFC (-0.01,-0.02)

## Slide 7: Format
Header
  Timeset
    It is name of timeset and should exist in timeset folder or test program.
  Voltage Category
    Syntax : [Dc_category] [Dc_selector]
    Example : BinCut_X_X_X LV
  Pattern#
    Can be generic pattern or pattern name with date code
    Example :
      PP_OTC_C_IN01_BI_CXXX_BST_JTG_XXX_ALLFV_SI_SRVE_SMT
      PP_OTC_C_IN01_BI_CXXX_BST_JTG_XXX_ALLFV_SI_SRVE_SMT_5_A0_1906290401
  Pins or Variable
    It can be power pin in pin map or variable in AC spec. Tool will base on Start/ Stop/Step to create Characterization condition.
    Start/Stop/Step
      Allow unit : V,mV,uV,Hz,KHz,Mhz
      Example : 0.75mV

## Slide 8: Format
Header
  Order
    Define sequence of X-axis and Y-axis for 2D shmoo, use comma as delimiter.
    Example: VDD_ECPU,VDD_PCPU
  Search
    Define the name and arguments of search algorithm for shmoo, and use comma as delimiter.
    Example: Jump 6;Linear
    PS. The algorithm of 2D shmoo’ Y-axis can not be jump.
  Temp. Condition
    Ongoing

## Slide 9: How to start/stop Auto Test System
Application Start
1) Click Watching Button and hide tool in taskbar.
Application Stop
1) Click tray icon in taskbar.
2) Click “X” to close the application.

## Slide 10: Environment Setting
MailTo
  Define mail list for result by “,”
TestProgram
  Define original test program, and it be executed correctly.
PatternFolder
  Default is [Path of TestProgram]\Pattern
  Define Pattern/TimeSet/HardIP_AutoGen_Info_All.txt.
PatternSync
  Define sync *.bat to catch the latest patterns from Fuji.

## Slide 11: Environment Setting
JobName
  Define job by user.
LodID
  Define lot ID
WaferId
  Define wafer ID
SetXY
  Define start location of test.
EnableWords
  User can define enable words in the flow.
Sites
  User can define test site in test program.
DoAll/OverwriteFailStop
  Turn on do all function for offline debug.
Select enable word from program

## Slide 12: Watching Folder
C-Autogen test plan
  Provided by user
Process log
  Tool records history and errors when processing or program validation.
Setting.ini
  Created by test environment window for test environment setting.

## Slide 13: Output Folder
DataLog
  The name is [origanl_test_plan_name]_[JobName]_[date_code].txt
Shmoo Report
  The name is [origanl_test_plan_name]_[JobName]_[date_code]_Shmoo.xlsx
Process log
Setting.ini

## Slide 14: Pattern Sync Setting
Max Pattern Wait Time(min)
  Default 30 mins
Pattern Checking Peroid(min)
  Default 3 mins / one time

## Slide 15: Environment check
Check if U:\TP-to-C651\PatternValidation\Input can be access
Check if U:\TP-to-C651\PatternValidation\Input\TesterStatus.xlsx can be access
Check to close all excel and Igxl before watching.

## Slide 16: Input Check
Check if there setting.ini in input folder.
Check if pattern is existed in dashboard.
Check if pattern is existed in pattern folder.
Check if “pattern_dashboard” sheet is existed in test plan
Compare enable word in data log and user definition.
Add type of error for debug
  Input,
  Environment
  Code