## Slide 1: PMIC T-Autogen Introduction
Jeff Li

## Slide 2: General Flow
New Kick Off
TestPlan
SCGH
PatList csv
VBT gen tool
OTP file
Hardware
-Using PA file to generate
1) Channel Map
2) Pin Map
T-Autogen
Error Report
Test program
File Naming Convention :
Test plan: [ProjectName]_*_TestPlan_*.xlsx
SCGH: [ProjectName]_*_scgh_*.xlsx
Pattern List: [ProjectName]_*_Patterns_List_Ext_*.csv
VBT gen tool : *VBT_Gen_Tool_*.xlsm
OTP file : *.otp or *.yaml

## Slide 3: Input File
Click “Load Materials” button, and select PMIC input file
  Test Plan => For all blocks
  SCGH Pattern List => For Scan, Mbist, OTP
  Pattern List Csv => For pattern, TimeSet
  VBT Gen Tool => For LDO, Acore, Buck
  Otp File (*.yaml / *.otp) => For OTP

## Slide 4: Test Plan Sheet Summary
Category | Item No. | Naming Convention | Description | Must/ Optional
Continuity | 1 | DCTEST_Continuity | Define DC test flow and Open/Short Limit | ●
Pin Map & Group | 1 | IO_Pinmap | To generate Pinmap | ●
 | 2 | ChannelMap | To generate Channel map | ●
 | 3 | IO_PinGroup | Define all I/O & Power pin groups used in Test Plan | ○
Power | 1 | VDD_Levels | To generate DC spec/Level sheet | ●
 | 2 | IO_Levels |  | ●
IDS | 1 | PMIC_IDS | Define IDS test, the format is the same as HARDIP | ●
Leakage | 1 | PMIC_Leakage | Define Leakage test, the format is the same as HARDIP | ●
DCTest | 1 | DCTEST_XXXX | Define DC function test, the format is the same as HARDIP | ●
Flow (2 choose 1) | 1 | GenMainFlow | Define Main flow by user definition | ○
 | 2 | Flow_Main | Define Main flow for all Test stage | ○
OTP | 1 | AHB_register_map | To generate AHB_register_map for OTP | ●

## Slide 5: SCGH Sheet Summary
Category | Item No. | Naming Convention | Description | Must/Optional
SCAN | 1 | SC_PC | To generate Flow/Instance for SCAN | ●
BIST | 2 | BI_PC | To generate Flow/Instance for MBIST | ●
DCTEST_XXXX | 3 | PMIC_PC | To define pattern used in DCTEST | ●

## Slide 6: Pin Map and channel Map
GUI of PinMap tool

## Slide 7: Pin Map and channel Map
Format of PA
  Site : To define site for multi site test.
  Bump Name : This is pin name in pin map and channel map.
  Assignment : To define the channel of pin in channel map.
  PS : User can specify this pin is power pin by using syntax “power”.
  Type : To define the type of pin in channel map. (ex. I/O,DCVI,GND,Utility)
  ChannelMap Name: To rename or merge the pin name. (ex. BUCK0_LX1_0 & BUCK0_LX1_1 use the same channel and merge into BUCK0_LX1) If channelMap Name is empty, tool will use Bump Name as pin name.

## Slide 8: Pin Map and channel Map
Format of Tester config
  Tester config is used to define the slot of instrument
To generate Pin Group
  Base on the instrument type in tester config tool will generate All_[instrument type]. (ex. All_IO,All_UVI80)
  To generate DCVI pin group (ex. DCVI for power pin group and DCVI_Analog for Analog pin group)

## Slide 9: Pin Map and channel Map
Same channel pins
  Tool will modify the channel name (ex. S:IDAC_OUT_0_DC30) when the channel are the same.
Rule for PMIC only
  If the channel type is “DCVI”, tool will generate the secondary pin for DCDiffMeter & DCTime with the same channel as below.

## Slide 10: Global Specs
T-Autogen will use “VDD_Levels” sheet in test plan to generate global Specs, including LV/NV/HV/HV2 and power sequence for power up.
Other Specified Global Specs
  SCAN_Speed : 16000000 (hardcode)
  SCAN_Period : =1/_SCAN_Speed
  Mbist_Speed : 16000000 (hardcode)
  Mbist_Period : =1/_Mbist_Speed
VDD_Levels sheet

## Slide 11: DC Specs / Level Sheet
T-Autogen will use “VDD_Levels” sheet in test plan to generate DC Specs/Level Sheet.
  Default categories : Common, IDS, Conti, Leakage, nWire, Scan, BScan, Mbist, Analog DC Categories.
  If user want to modify original DC spec or to create new DC spec, user can use “POWER_OverWrite” to generate DC Spec/Level Sheet.
Power_overwrite will change from formula to fixed value.
DC spec
formula base
Fixed
POWER_OverWrite

## Slide 12: DC Specs / Level Sheet
“IO_Levels” sheet will
  Add level rows for IO pins.
  Generate Pin group by Domain column (ex. VDDIO)
Level sheet
Level sheet Name
Valid headers are Domain,VDD,VIH,VIL,VOH,VOL .
IO_Levels
Pin Group

## Slide 13
Backup

## Slide 14: AC Specs
AC category generation rule :
  Free Running Clock variable : T-Autogen will generate by “FreeRunningClock” in Settings\Basic\nWire_and_relay_[ProjectName].xlsx
  TimeSet variable : T-Autogen will follow SOC rule to add customized variable into AC spec by TimeSet.
Follow SOC rule.
Skip at least 1 line after the last tset line
Use header : /* Var Definitions */ to denote start of variable declaration portion.
Generated AC Category | Assigned Block | TimeSet Name
Common | Remaining other blocks | TIMESET_*_*_JT_*_*
BScan | DCTest | TIMESET_*_*_IO_*_*
Scan | Scan | TIMESET_*_*_SC_*_*
Mbist | Mbist | TIMESET_*_*_BI_*_*

## Slide 15: Scan and Mbist
Flow
Needed sheets in SCGH:
  SC_PC : scan prod char sheet
  BI_PC : Mbist prod char sheet
Flow/Instance Generation:
Input File : SCGH: SC_PC /BI_PC
Instance

## Slide 16: LDO/Acore Work Flow
Gen. SubFlow sheet
Gen. Instance sheet
Gen. LDO/Acore VBT
Gen. Bintable
sheet
Read input file
VBT gen tool/test Plan
Merge & Gen. IGXL
Trigger macro to generate VBT
Autogen Tool
VBT gen tool

## Slide 17: LDO T-Autogen
Input file : VBT generate tool & Test plan
  (FileName format : *VBT_Gen_Tool_*.xlsm)
LIB path : To get relative test info. for VBT gen tool to generate VBT.
(Default path : BasLibraryPath in Setting.ini & \PMIC\LIB)
VBT Output path : To place created VBT modules to generate new test program. (Default path : User’s specified output path & \IGLink\trunk\Module\LibraryConding)
Customized VBT : To copy all *.bas/*.cls in VBT_Gen_Tool into new test program.
=> Copy modules/Classes from VBT_Gen_Tool
=> LIB path is D:\LibBas\PMIC\LIB

## Slide 18: VBT generate tool
Sheet name
Sheet Name :
  B1 cell starts with “TEST PLAN FOR <“ & sheet name ends with “_ sequence number” can be identified as test plan sheet, and flow will order by this sheet sequence.
SubFlow Name :
  First key word of flow name will be used as block name. (eg. Only block name “LDO” can be generated by LDO block.)
  T-Autogen will used the full flow name to generate sub flows.(eg. Flow_LDO_TRIM, Flow_LDO_POSTBURN)
Instance / VBT function Name : T-Autogen will generate instances when command was “start_of_test”.
Full flow name
Instance/ VBT function name

## Slide 19: Syntax Check
Pin Name : Check if the pin name can be found in pinmap.
Pattern Name: Check if the generic pattern name, that’s command is “TEST_SET_UP_PATTERN”, can checked if it can be found in pattern list Csv.
Bit Field Name : Check if the bit field name can be found in AHB Register Map.
AHB Register Name : Check if the AHB register name, that’s command started with “AHB_WRITE” or “AHB_READ”, can be found in AHB Register Map.
Bit field name
AHB register name
Pin name
pattern name
Error Report

## Slide 20: Test number in subflow
T autogen will base on the table in “Block_TestNumber” sheet of \Settings\Basic\TN_Assignment_[project].xlsx to generate Test number in subflow.
User can define test number in the each subflow sheet by start, end and step column.

## Slide 21: Bin number
T autogen will base on the table in DC_HardIp_Bin_Def sheet of BinNumberConfig_PMIC.xlsx to generate Bin number.

## Slide 22: OTP
Input file : OTP files(*.otp/*.yaml)
Output file:
  Use OTP files to generate “OTP_default_reglist” & “OTP_register_map” & ”GlobalAddressMap”, that will be loaded by OTP VBT.
  Use “PMIC_PC” in SCHG file to generate to patSet.
  Merge the standard subflow and instance sheet into test program.
  (\Settings\eFuse\Efuse_Flow_TestInst_[ProjectName].xlsx)
OTP_default_reglist
GlobalAddressMap
OTP_register_map

## Slide 23: Free Running Clock
T-Autogen will use “FreeRunningClock” table to generate free Running Clock variable into AC specs and TimeSet.
Settings\Basic\nWire_and_relay_[ProjectName].xlsx