## Slide 1: PMIC_BinCheck_Request
Teradyne Confidential
20211217

## Slide 2: How to use
Step 1. Please prepare your program. Step 2. Execute Bin check tool with IGXL environment. Step 3. Check Report file.

## Slide 3: Check point Review

## Slide 4: Check point 1
Step1 : Find the “Bintable” opcode in subflow, get the parameter name for this bintable
Step2: Search the Bin table sheet to get the control flag name setting for Bin table name
Step3: Search the control flag name in subflow, check is it define in same subflow. Also the Bintable sequence need to be correct.
Each sub flow
Bin table sheet
Each sub flow
1
2
3

## Slide 5: Check point 2
Step1 : Find the bin name in bintable.
Step2: Search the Bin name in all of flow sheets. Check is it called by any sub flow sheet?
Also need to check SW bin number in “Bin table sheet”. Is any duplicate?
Bin table sheet
Each sub flow
1
2

## Slide 6: Check point 3
Step1 : Find the “set-error-bin” opcode in each flow, get the error bin number.
Need to list the flow which without the error bin setting.
Step2: Search Bin table sheet to get the match SW/HW bin number.
If match need to list which subflow using this error bin.
If no match in bintable, need to report it.
Each flow
Bin table sheet
1
2

## Slide 7: Check point 4
Step1 : Check all flow sheet about the sort bin, hard bin and result have set.
List all of items which have set. (For this case, the test item do not need to set bin table)
Step2: Check VBT code about(next phase)
TheExec.sites.Item(Site).TestResult =siteFail
TheExec.sites.Item(Site).SortNumber = ??
TheExec.sites.Item(Site).BinNumber = ?
Each flow
1
All VBT code
2

## Slide 8: New Feature of Check Point

## Slide 9: Check point 5-Standard Bin Check
Step1 : User can list the standard bins to Config file by Project.
file path:(.\Config\Fail_Stop_Table.txt).
Step2:
Standard Bin Check rule is based on soft bin number as the basis for comparison.
All of the soft bin which define in config file need exist in program.
Config file
1
Bin table sheet
2

## Slide 10: Check point 6-Fail Flag Symbol Check
Step1 : Check the value of all Flag Symbol.
Flag of Normal Bin: only F or T (Red Frame will show fail.)
Flag of Standard Bin: Only T (Red Frame will show fail.)
Bin table sheet
1
All Bin Flag Check
2

## Slide 11: Check point 7-No Bin Out Check
Step1 : Check the Flag of test item exist or not.
If bin flag is empty, report Item NoBinOut.
If the flag exists, check any relative bin name use same flag. If not, report Item NoBinOut.
If the bin name not exist in same flow, list Item in the report.
Step2 : Check any gating rule of Opcode “BinTable”.
If there is any rule in the BinTable, list Item in the report.
Each sub flow
1
Bin table sheet
2
Each sub flow
3
Flag is empty
BinTable with condition

## Slide 12: Check point 8-No Bin Out Check Reference Datalog
Step1 : Offer a datalog that log from test program.
Step2 : Check Method is as same as Check Point7 and list Item in the report(NoBinOut ReferenceDatalog).
Each sub flow
1
Bin table sheet
2
Each sub flow
3
Insert the datalog you want to check
Insert the program you want to check

## Slide 13
Output report-BinOut Sheet
Bin Name
Flag Name
SubFlow
Check Point

## Slide 14
Output report
To check each sub flow the error bin setting
Check Point: Is any function setting the Bin number in flow sheet?
Check Point: Is any function setting the Bin number in VBT code?

## Slide 15
Output report-NoBinOut Sheet
This sheet will list NoBinOut check result and show the reason in Comment Column.

## Slide 16
Output report-NoBinOut Sheet
This sheet will list NoBinOut-ReferenceDatalog check result and show the reason in Comment Column.

## Slide 17: END
Notes: Add a summary page of improvements