## Slide 1: Gen DC Support User Manual

## Slide 2: Gen VBT
Purpose
  To use universal table and template to generate Bas file
GUI
  Output File : Table’s file name + “.Bas”

## Slide 3: Gen VBT
Refill excel file from Bas.
  -Output excel file from the .bas content

## Slide 4: Gen VBT
Get template file
  Use Template button — Chose template file and path

## Slide 5: Gen VBT
Basic concept
  Fill test pin in PinName column
  Enum is according to table sequence in Bas.
  SP_PinName is according PinName content which is test pin
  SPForceI is according to SpecificLimit value which is Force I value
  Wait_Time is according to SpecificWaitTime value

## Slide 6: Gen VBT
Basic concept
  Switch relay need to fill in On_Relay & Off_Relay
  When testing disconnect pin need to fill in MustDiscnctPins
  Ex.ADC_IN needs to be disconnect with PPMU and Digital when ADC_IN_UVI80 testing.

## Slide 7: Gen VBT
Basic concept
  When testing want to setup other pins need to fill SpecCondiPin and SpecCondiPinVolt_Current
  E.X Setup AMUX_AY_DC30 to V = -1.5V and I =0A when AMUX_AY testing

## Slide 8: Gen VBT
Basic concept
  TestItem default use “Both” or Instance tail name as setup keyword

## Slide 9: Gen VBT
Need to enable GenLeakPinDic and GenContiPinDic in OnProgramStarted and OnProgramValidated
  Output file(Bas.) included GenLeakPinDic and GenContiPinDic function

## Slide 10: Gen VBT
Merge the output file into test program
  Insert output file(Bas.) to program

## Slide 11: Gen VBT
Enable function in the VBT code of Conti test
  Enable Conti_PerPinSetting_beforeMeasure and Conti_PerPinSetting_afterMeasure in VBT_LIB_DC_Conti_PMIC module

## Slide 12: Gen VBT
Enable function in the VBT code of Leakage test
  Enable Leak_PerPinSetting_beforeMeasure and Leak_PerPinSetting_afterMeasure in VBT_LIB_DC_Leak_PMIC module

## Slide 13: Appendix