## Slide 1: Autogen Profile Insertion Tool Current/Voltage Profile

## Slide 2: Outline
  Autogen Profile Insertion Tool
    Insert current profile instances
    Data Analysis
  VBT Modification for current/voltage tool
    Sample Rate and Sample Size Criteria
    Measurement Criteria
    Alarm Mechanism
  Future
  Notice

## Slide 3: Autogen Profile Insertion Tool
There’re two functions in this tool:
Insert current profile instances in the test program.
  Choose the ByFlow or ByInstance to insert the profile’s test instance for each flow table or each test instance independently.
Data Analysis for the current profile output files.
  Remove current pulses which are supposed to be caused by the power capacitance.
1
Test Program Modify tab
2
Data Analysis tab

## Slide 4: Test Program Modify tab - By Instance
1. Input execution profile, test program and select the Channel Map
2. Choose the button “ByInstance” to insert the profile’s test instance for each test instance.
3. Click button “Run “ to generate a new test program.
Start
Plot
Test Program Modify tab
1
2
3

## Slide 5: Test Program Modify tab - By Flow
1. Input execution profile, test program and select the Channel Map
2. Choose the button “ByFlow” to insert the profile’s test instance for each flow table.
3. Click button “Run “ to generate a new test program.
Start
Plot
Test Program Modify tab
1
2
3

## Slide 6: Test Instance Introduction
There are the test instance in the sheet “TestInst_Profile”,
PinName: Define which pin we want to plot.
WhatToCapture: Select current profile(I) or voltage profile(V).
CapSignalName: Give the name for the capture signal.
Plottime: How long we want to capture the signal, the default unit is second.
ByFlow(optional): Show the Flow sheet name in the test log if it is TRUE. Default is False.
SampleRate(optional): Setup the fixed value if Plottime is empty.
SampleSize(optional) : Setup the fixed value if Plottime is empty.

## Slide 7: Input Parameter - Core Power Pins(optional)
With the user-definition file, the measurement power pin will follow the list and append the specified power pins which is measured in the flow.
Without the file, the measurement power pin will list all the power pin whose instrument is DCVS.

## Slide 8: By Instance - Export File Naming Rule & Test Log
File name need to follow the rule.
  Profile – Site – Pin – Sample rate – Sample Size – [By Instance]– DayCode.txt
Analyze the data to find the maximum, average and AverageLast10per.
  Test log needs to follow the rule.
    [By Instance]_CurrentProfile[Maximum/Average/AverageLast10per]
By Instance
By Instance

## Slide 9: By Flow - Export File Naming Rule & Test Log
File name need to follow the rule.
  Profile – Site – Pin – Sample rate – Sample Size – [By Flow]– DayCode.txt
Analyze the data to find the maximum, average and AverageLast10per.
  Test log need to follow the rule.
    [By Flow]_CurrentProfile[Maximum/Average/AverageLast10per]
By Flow
By Flow

## Slide 10: Data Analysis tab – Chart Group by Individual
1. Input the current profile path which stores the per each pin’s data collection.
2. Choose the “individual”, it produces the single graph per each exporting profile file and store in the power point report.
3. Filter rule to select the customized configurations to remove the unwanted pulse. It shows two graphic, one is the original and the other is modified one in the power point report and the raw data will be saved in the excel.
1
2
3
Remove the unwanted pulse caused by capacitor
3. Filter Rule Introduction
a. Loop Cnt: How many times to remove the unwanted pulse.
b. Filter Width: To remove the pulse whose width is lower than the Filter Width.
c. Sepc(Stdev): Filer Criteria to find the 100 points on the left and right sides of the pulse, and calculation the standard deviation.
d. Only Last: Show the original graph and the graph which removed the unwanted pulse in the last Loop Cnt.

## Slide 11: Data Analysis tab – Chart Group by Individual
1. Input the current profile path which stores the per each pin’s data collection.
2. Choose the “Merge”, it composites all the single graph per each exporting profile file and store in the power point report.
1
2

## Slide 12: Data Analysis tab – Power Consumption
1. Select “ChartByPower”, you should input current profile path both current and voltage .
2. Choose the output format, “Individual” or “Merge”,
1
2
1

## Slide 13: Data Analysis tab – MaxSummary

## Slide 14: Data Analysis tab – conti.

## Slide 15: VBT Modification for current/voltage tool
  VBT Modification for current/voltage tool
    Sample Rate and Sample Size Criteria
    Measurement Criteria
    Alarm Mechanism

## Slide 16: Sample Rate and Sample Size Criteria
1. If the plottime is larger than the limitation of instrument, the sample size and sample rate will be the maximal one of instrument .
2. If the plottime is smaller than the limitation of instrument, it will obtain the current sampling rate. Then, find the optimal sampling rate by looping the size of degree and calculate the optimal sampling size.
1
2

## Slide 17: Measurement Criteria
Bypass the power pin’s current measurement while we are profiling current or voltage that power pin.
Note: error DCVS:0070 will occur because the instrument can not capture and meter strobe at the same time.

## Slide 18: Alarm Mechanism
Bypass the overrange alarm while we are profiling current or voltage that power pin.
Note: alarm DCVS:0075 overrange alarm happened because the alarm window open during the instrument measurement when the voltage translation.

## Slide 19: Notice
  System Memory Limitation
  Header/Footer mismatch with Flow sheet name
    Ex: Header: SocSa_Header_1 , Flow sheet name: Flow_SocScan_Sa
  Miss Header/Footer at BinCut Flow in Project T-sic, but they exist after Project T-sic.